## Slide 1: Video System
110061562 呂依凡
Github: https://github.com/EvanLu0815/HLS/tree/main/LABB_video_processing

## Slide 2: System Introduction
host
Main.cpp
kernel
Video_2dfilter
filter
video_filter_rescale
PixelIni
PrintPixel
pixel_in 20* 20
pixel_out 20* 20
3*3 window
1*1 pixel

## Slide 3: System Introduction
Host
Generate pixel_in
Print the pixel_in
Rescale pixel_in
Print the rescaled pixel_in
Pass the pixel_in to kernel
Print the kernel results, pixel_out
Kernel
Video_2dfilter: prepare 3*3 window for filter
Filter: Do MAC (multiply accumulate)

## Slide 4: Introduction to Algorithm filter
window
h
*
=

## Slide 5: Introduction to Algorithm video_2dfilter
(0, 0) | (0, 1) | (0, 2) | … | … | (0, 19)
(1, 0) | (1, 1) | (1, 2) | … | … | (1, 19)
(2, 0) | (2, 1) | (2, 2) | … | … | (2, 19)
… | … | … | … | … | …
(19, 0) | (19, 1) | (19, 2) | … | … | (19, 19)
Lots of memory access!

## Slide 6: Synthesis Report Timing
The clk frequency 10ns has been met.
Top function spend 10877 cycles to complete write all outputs
Initiation interval is 27 row_loop_col_loop has been pipelined.

## Slide 7: Synthesis Report Utilization

## Slide 8: Optimize Design 1 rewind
Top function has prepared for next input after 10800 cycles

## Slide 9: Optimize Design 1 enable_flush
Number of registers decreases about a half for LUT. The pipeline will not stall after adding enable_flush, that is, it do not need to keep the outputs during pipeline stall.

## Slide 10: Optimize Design 2 Using Line Buffer
Line buffer
Pixel_in[row][col]
col
col + 1
col - 1
Access only one pixel!

## Slide 11: Optimize Design 2 Timing/ Utilization

## Slide 12: Optimize Design 2 rewind
Top function has prepared for next input after 400 cycles

## Slide 13: Optimize Design 2 enable_flush
The report remains the same.

## Slide 14: Optimize Design 3 Extending the iteration domain
Loop bound is increased by 1 in this case
Read the first pixel in the first iteration, but write the first output in the next iteration.
 Allow the filter to be implemented without spatial shift.
  Prepare window in the previous iteration

## Slide 15: Optimize Design 3 Timing/ Utilization

## Slide 16: Optimize Design 3 rewind
Timing violation occurs! 9.947 + 2.70 = 12.647 > 10ns

## Slide 17: Optimize Design 3 enable_flush
The report remains the same.
Timing violation remains!

## Slide 18: Optimize Design 3_2 Adjust the Operation Order
Move the function call of filter() to the beginning of the pipeline body
 Truly realize avoiding spatial shift

## Slide 19: Optimize Design 3_2 Timing/ Utilization

## Slide 20: Optimize Design 3_2 rewind

## Slide 21: Optimize Design 3_2 enable_flush

## Slide 22: Optimize Design 4 Handle Boundary Condition
Avoid the window access beyond boundary
Re-access the pixel on the boundary when window will access those beyond boundary pixels.
Handling the boundary condition causes the hardware more complex and time consuming.

## Slide 23: Optimize Design 4 Timing/ Utilization

## Slide 24: Optimize Design 4 rewind

## Slide 25: Optimize Design 4 enable_flush

## Slide 26: Observation and Learning
We cannot achieve II = 1 when we access 3$\times$3 pixels from pixel_in for each time we call filter.
We can achieve II = 1 when we access only one pixel from pixel_in for each time we call filter.
rewind will help to decrease the latency that main function prepares to access the next input.
enable_flush will not help to decrease the loop latency in some cases.
When flush the pipeline, the pipeline will shut down all the successive stage until the final input has been processed.
   If the time of pipeline stalling is shorter than or equals to that of completing all the older inputs and resume pipeline, enable_flush is not a good choice.
When the if-statement containing memory access, rewind and enable_flush are useless. They will cause timing violation.

## Slide 27: Problem
I had no background knowledge about video processing. I spent lots of time to understand the must-known knowledge about video.
When I did this lab, I quickly find that I did not "fully" understand the pipeline rewind and flush. I looked up for those information that I am not quite familiar with.
Additionally, I utilized my understanding about memory access to analyze the timing violation about the 3rd and 4th algorithm, which I really spent lots of time to analyze.